## Slide 1: IN-SITU GONE OVERBOARD AND OTHER INNOVATIONS
Roger A. Failmezger, P.E., F. ASCE, D. GE
Geo-Kansas City Annual Meeting
April 5, 2019

## Slide 2: Outline
Performance and Financial Failures
  Why we need accurate measurements and design models
Harry Nice Bridge
  Route 301 over the Potomac River
  Heavy Seafloor Direct Push System—like performing soundings on land
Calvert Cliffs Power Plant
  Performing a 400 foot deep Dilatometer Sounding—Deepest ever done
Cyclic Borehole Shear Test
  In Development (Dr. Jeramy Ashlock—Iowa State University)
  Dynamic Shear Strengths/Residual Shear Strengths

## Slide 3: TYPES OF FAILURES
Performance Failure
  Outcome has an undesired consequence
Financial Failure
  Poor design model and parameter evaluation creates overly costly design because of high uncertainty/lack of knowledge
    Settlement Evaluation
      Need Static Deformation Test => Dilatometer, Pressuremeter, Lab Consolidation Test
    Vertical Pile Capacity
      CPT ideal model/PMT for stronger soil/rock
    Lateral Pile Capacity
      Need Lateral Test—DMT/PMT
Never Want the Test to be Your Source of Uncertainty
Accurate Design Balances Performance and Financial Failures– Select the Appropriate Probability of Success

## Slide 4: Probability of Success
Because of uncertainty, design solution is not deterministic, but rather probabilistic solution based on a bell-shaped curve
Bell-shaped curve is defined knowing:
  Average Value
  Standard Deviation
  End Limits
Beta probability distribution curve gives engineer best solution—Choose the end limits
Total area under curve must always equal 1.0
Probability of success is the area under curve in the success zone

## Slide 5: Same Soil—Different Tests and Modeling

## Slide 6: Lack of KnowledgeMore Expensive Design Probability curves shift to the right for same Success

## Slide 7
Plot Average Factor of Safety and its Standard Deviation to Determine Probability of Success

## Slide 8: Dilatometer Predicted Settlements
{After Schmertmann (1986) and Hayes (1986)}
COV = 0.18

## Slide 9
SPT N60
Sands Only
COV = 0.67
(After Burland and Burbridge, 1985)
Financial Failure Will Certainly Occur!

## Slide 10: Harry Nice Bridge Subsurface Investigation
Performed CPT, DMT, PMT, VST, SPT and Seismic with True Interval (0.50 m) DMT Module
Discuss what techniques we used to more efficiently perform these tests
Compare the undrained shear strengths and deformation moduli from the tests
  Tests were performed in clusters at the north and south ends of the channel

## Slide 11
Subsurface Information from 1939

## Slide 12: 15-Ton Capacity Seafloor Direct Push System
Base Area = 192 sq. ft.

## Slide 13
Using Spreader Frame to Keep Slings Vertical

## Slide 14
Seismic Hammer
Lowering Direct Push System

## Slide 15
Performing Dilatometer Tests Using Seafloor System

## Slide 16: Advantages of Seafloor Direct Push —Like Pushing on land
Testing starts at the mudline
  Measure the strength and deformation properties of very soft muds
3-inch casing attached to the top of the seafloor system and extended to the barge deck serves as fixed reference to measure the tests depths
  Does not move with either waves or the tide and provides accurate measurements
  Attached hydraulic and air hoses, load cell and camera cables to casing
Rod pushing avoids zone between barge deck and mudline of parasitic rod buckling or lateral movement of casing
Probes are pushed at a constant 2 cm/sec rate satisfying ASTM
  Waves do not alter this rate or cause pinching of cables

## Slide 17: Pressuremeter Tests
Used Texam Unit and performed strain controlled tests
  About 40 data measurements/test
Measured pressures with a digital gauge—accurate to 1 kPa
Used 74 mm tri-wing bit for cohesive soil and 76 mm tri-cone bit for cohesionless/cemented soil
  High quality borehole critical—experienced drillers important

## Slide 18
Chart: Corrected Pressuremeter Test Results
| 0 | 0.89947208862071193 | 1.8148372564761095 | 2.7123666184338147 | 3.5786912309591745 | 4.3834970347804925 | 5.090917609901946 | 5.7571161761696965 | 6.4166712789398117 | 6.4105125715461009 | 6.3576064286733569 | 6.255090532695351 | 6.3655752046421155 | 6.4676452151565478 | 6.577574540956066 | 7.1908981918616721 | 7.9349218943756794 | 8.6377892492690336 | 9.3853379064370301 | 10.14400824693773 | 10.161304387969739 | 10.129036156285732 | 10.092037469538084 | 10.115888563175846 | 10.144950244800599 | 10.22866625471519 | 10.927017154803732 | 11.714746487217486 | 12.494100776240892 | 13.29209956390962 | 14.071956390289397 | 14.092579200320987 | 14.083150411053214 | 14.041535670745686 | 14.047625653293338 | 14.069020730456128 | 14.161642166260545 | 14.876304096445004 | 15.647754010126636 | 16.431924821020893 | 17.209851516531536 | 17.981409759545986 | 18.750171194786059 | 19.524018932946706 | 20.286081906364693 | 21.03754908802642 | 21.795184002410473 | 22.550282564930193 | 23.300282642971439
Corrected PMT Results | 8.4345 | 8.6125 | 8.8305 | 9.3945 | 10.7945 | 14.1345 | 20.7705 | 28.7265 | 36.7685 | 27.6315 | 21.8645 | 17.9155 | 22.6445 | 26.9215 | 30.9085 | 40.4565 | 45.0545 | 50.9925 | 55.0905 | 58.5785 | 48.4115 | 41.9645 | 35.3975 | 43.6545 | 50.5515 | 55.3885 | 60.9465 | 62.9245 | 65.0165 | 66.1785 | 67.8305 | 57.4825 | 50.0645 | 43.9165 | 52.7945 | 59.9525 | 64.3305 | 68.3125 | 69.8745 | 70.7265 | 71.6185 | 72.5625 | 73.4185 | 73.8645 | 74.5865 | 75.5485 | 76.0645 | 76.4945 | 76.9445

## Slide 19: Vane Shear Tests
Used AP van den Berg I-VANE
Vane Motor at bottom of hole turned vane and measured torque
  No parasitic rod friction
Computer at surface reads values from connecting cable and displayed results while performing test
Peak: turned vane 0.1o/sec for ¼ revolution
Rapid turning 6o/sec for 10 revolutions
Remolded: turned vane 0.1o/sec for ¼ revolution

## Slide 21: Standard Penetration Tests
Used 125 mm diameter steel casing telescoped inside 200 mm diameter steel casing
Added bentonite and polymers to the river water to make drilling mud—added soda ash to reduce the pH
Used NWJ drill rods (35 mm ID) for good mud circulation
Drill rods and steel casing were quite heavy for drill crew to maneuver
  Used crane on barge to either lower or remove them from hole
  Drilled lowered front jacks moving drill derrick out of way
  Crane could handle 110 feet (34 m) with each of its two hoists
Crane significantly improved efficiency of drilling/sampling operations

## Slide 23: True Interval Seismic Tests
Contract required both compression and shear seismic tests to 55 meters below mudline
  Compression waves measured the speed through incompressible water (1500 m/s—wasteful)
Cemented layers prevented penetration from top to bottom
Drilled 125 mm hole to 56 m
Lowered SDMT probe to 55 m carefully aligning sensors
Backfilled with washed fine gravel about 5 m above test
Performed seismic tests (multiple strikes) and then raised probe 1 m for next test
Used large hammer from seafloor to generate waves

## Slide 24
SOUTH END OF RIVER CHANNEL
Enlarged scale for upper 15 meters
North Side

## Slide 25
SOUTH END OF RIVER CHANNEL

## Slide 26
NORTH END OF RIVER CHANNEL
Enlarged scale for upper 15 meters
South Side

## Slide 28: Bridge Conclusions
Seafloor direct push system efficiently pushed DMT and CPT—like performing them on land—the way to go!
Successfully measured seismic waves with true-interval seismic DMT probe and seafloor hammer to 58 meters below mudline
Undrained shear strength and deformation modulus values compared favorably with DMT, PMT, VST and CPT with properly chosen correlation factors
Adjust the investigation as data are collected
  1939 data—inadequate—show sandstone instead of cemented sand layers
  Upper clays much softer than thought
  Lower soil much stiffer and stronger than thought—needed more pressuremeter tests
Ideally, investigations could include direct push sounding and soil boring adjacent to each other and performed simultaneously
  If direct push sounding has penetration refusal before desired depth, perform pressuremeter tests in boring to get high quality data in that missing in-situ test zone
  Best use of costly barge time

## Slide 29: Lessons Learned
Job has much stress because of high barge costs
  Work with people that you like
  Get the best and most experienced drillers and engineers
Modifying Seafloor System
  Using 10 foot long N-rods—structural section modulus 2.3 times large CPT rods—push with much more thrust without buckling risk
    While heavier only 1/3 number of joints
  Seismic hammer with hydraulic trip lift
  Compression or P waves waste of time
  Build a 16 foot by 16 foot structural frame with fold down decking on side of barge for safer working platform
  Lower Seafloor system through this framed hole—minimizes crane reach
Drug and alcohol testing for barge crews
  Crane operator caught at end of job smoking marijuana

## Slide 30: Performing a 400-foot deep Seismic Dilatometer Sounding

## Slide 31: DMT Project Requirements
Perform DMT at 1 foot depth intervals to 400 feet
  We convinced the client to perform tests at 20-cm intervals (5 tests per rod) because it would not take much more time to do so and 50% more information would be acquired
Perform true-interval seismic tests at 1-m depth intervals until shear wave attenuated
Perform pore pressure dissipation tests
Obtain “C” readings below the water table

## Slide 32: Direct Push Method
Impossible to successfully perform to full depth
Cemented sand layers would cause penetration refusal
Sounding would be too inclined from vertical
Would develop high rod friction

## Slide 33: DMT Torpedo

## Slide 34: DMT Torpedo Method (cont.)
DMT cable was threaded through the AW rod and then exited to outside of the rods
  Rubber washers around rods to give lateral support
Used an adapter to NWJ rods
GeoServices lowered the DMT torpedo and NWJ rods to the bottom of the hole
  Used 20 foot sections of NWJ rods and a 5-foot long NWJ rod with welded 5/8 square stock (centralizer rod) between the 20-foot sections
  DMT cable was taped to the outside of the NWJ rods at 10-foot intervals
At the top of the NWJ rods, an adapter was used to channel the cable back into AW rods

## Slide 35: Centralizer

## Slide 36: DMT Torpedo Method (cont.)
GeoServices moved their CME-75 drill rig off of the hole
Moved In-Situ track rig back exactly over the hole
Camera was placed inside the hole in the track rig
Monitor with a cross-hairs was watched as track rig was repositioned over the hole

## Slide 37: DMT Torpedo Method (cont.)
AW rods had the same diameter as the In-Situ direct push rods
Existing In-situ clamp worked with the AW rods
Threaded DMT cable through the AW rods
Lowered BX-casing (3-inch OD) over AW rods to provide lateral support
Pushed DMT to test depths (20-cm intervals) and performed test

## Slide 38: In-Situ Direct Push Clamp

## Slide 39: DMT Control Unit and Auxiliary 100 Bar Gauge
Some pressure readings were higher than the standard 60 bar gauge—added a 100 bar gauge

## Slide 40: Drilling Equipment
Selecting the drill rig with the necessary accessories was critical to successful project
  High capacity Gardner –Denver piston pump
  3 different speed/capacity winches
  Hydraulic Break-out Wrench/Rod Clamp
    Footing
Extensive maintenance was performed on drill rig including rebuilding of pumps prior to mobilization

## Slide 41: GeoServices CME-75 Drill Rig

## Slide 42: Additional Drilling Efficiencies
Used a three person crew that had combined 70 years of experience
Used a large mud pit lined with plastic
Circulated the drilling mud through a desander to keep mud clean
Used steel saw horses to hold their NWJ rods in 20-foot sections

## Slide 43: Mud Pit

## Slide 44: NWJ Rods Kept on Steel Saw Horses

## Slide 45: Additional Drilling Efficiencies (cont.)
Used 4 hoisting plugs so that they could simply clip the winch line on rod and were never waiting for the rod to be hoisted
Used three winch cables
  100 feet of rod could be hoisted with light duty but fast winch
  100 to 200 feet of rod could be hoisted with the medium duty winch
  200 to 400 feet of rod had to be hoisted with the heavy duty but slower winch

## Slide 46: Additional Drilling Efficiencies (cont.)
GeoServices’ driller, Ronald Stidham, knew which winch to use when
At 400 feet, the GeoServices’ crew was able to trip either in or out of the hole in about 45 minutes
Used a reel to keep DMT cable from getting tangled

## Slide 47: DMT Cable Reel

## Slide 48: Satisfying Conclusions
Significant planning for a complicated project made the project go smoothly in the field
Selecting the most suitable equipment enabled the project to be successfully completed
Working with an experienced driller and crew eliminated many field frustrations

## Slide 49
Cyclic Borehole Shear Test (CBST)
Soil Testing Device

## Slide 50: The Problem
“Virtually every structure is supported by soil or rock. Those that are not either fly, float, or fall over.” –Richard L. Handy
Soil shear strength parameters (friction angle ’ and cohesion c’) are required for nearly ALL foundation design and slope stability problems
Shear strength parameters are typically obtained by
  Laboratory tests: time-consuming, results affected by sample disturbance
  Indirect empirical correlations to penetration test (SPT, CPT) indices: imprecise, not a direct measurement of shear strength
  Other in-situ tests, most of which measure a test index value, do not directly measure shear strength
Soil liquefaction susceptibility is also assessed using time-consuming lab tests, or in situ SPT, CPT, or shear wave velocity tests. None of these in situ tests actually simulate in situ the cyclic stresses and buildup of pore pressures that cause liquefaction.

## Slide 51: The Solution
In Situ Cyclic Borehole Shear Test (CBST) Device
  Applies controlled normal and shear stresses to soil through serrated plates in contact with borehole wall, which create soil-on-soil failure surfaces
  Applied shear stress can be monotonic or cyclic
  Can measure pore water pressure in soil during tests
  Monotonic test gives soil shear strength parameters
(friction angle ’ and cohesion c’)
  Cyclic test reveals soil behavior under repeated loading such as beneath bridge foundations or during earthquakes, can be useful for measuring residual shear strength parameters, cyclic behavior, and assessing liquefaction susceptibility

## Slide 52: In Pictures
Pressure Tubing and Pneumatic Cylinders: for pneumatic control of expansion of shear and anchor heads, and vertical actuation of cyclic shear head.
Expanding Anchor Head: expands against inside of hollow-stem auger, borehole wall, or borehole casing to provide reaction for pushing/pulling cyclic shear head below.
Load cells and displacement transducers: provide feedback for device control and data for analyzing soil response. Also enable additional test possibilities such as creep and consolidation.
Pressure transducer: measures soil pore water pressure during
testing.
Cyclic Shear Head: (1) expands horizontally to apply user-specified value of normal stress in soil, (2) moves vertically under selectable displacement- or stress-control to apply monotonic or cyclic shear stress in soil. Measuring peak shear stress for a range of normal stresses gives Mohr-Coulomb failure envelope of soil (’ and c’).

## Slide 53: Deliverables
CBST Device with Control Hardware and Software
  One prototype anchored shear head has been built, but software control program and electronic instrumentation/control system do not exist
  Development of software control program in LabVIEW
is most difficult task
Validation test results and comparisons to existing test methods
Prototype shear head component of CBST
Automated non-cyclic BST device showing the type of electronics and software control program that need development
Simpler shear head of traditional BST device sold worldwide by HGI (for comparison only)

## Slide 54: CONCLUSIONS
Choose the tests that best model the design needs
  Review case studies to evaluate accuracy of methods
Engineers should make the measurements because they understand the design needs
Technicians only collect numbers—do not have educational background to understand their meaning or make any field changes
Encourage you to vote for Dr. Jean-Louis Briaud
for ASCE President in May!