## Slide 1: Measuring and comparing soil parameters for the harry nice bridge
Roger A. Failmezger, P.E., F. ASCE, D. GE
Geo-Carolinas Conference
Charlotte, North Carolina
October 9, 2017

## Slide 2
Drs. John Schmertmann and Silvano Marchetti at DMT’15

## Slide 3: Subsurface investigation
Performed CPT, DMT, PMT, VST, SPT and Seismic with True Interval (0.50 m) DMT Module
Development of Heavy Seafloor Direct Push System—like performing soundings on land
Discuss what techniques we used to more efficiently perform these tests
Compare the undrained shear strengths and deformation moduli from the tests
  Tests were performed in clusters at the north and south ends of the channel

## Slide 4
Subsurface Information from 1939

## Slide 5: 15-Ton capacity seafloor direct push system
Base Area = 192 sq. ft.

## Slide 6
Using Spreader Frame to Keep Slings Vertical

## Slide 7: Barge Company’s Idea for Working Platform
Lowering Direct Push System
Lowered system below decking and swung system towards barge
Added rods and casing as system was lowered to seafloor
My new work platform system will have 16ft by 16 ft opening with hinged fold down decking
Mud was so soft that rods would have fallen by their weight up to 40 feet
Used clamp is pull position to lower rods at 2 cm/sec until mud could support their weight

## Slide 8: Seismic hammer system
Used large pendulum hammer with trip release from crane to generate shear wave
Used 300 pound donut hammer with trip release from crane to generate compression wave
  Worked but always found speed equal to 1500 meters/sec—speed of wave travelling through water

## Slide 9
PERFORMING DILATOMETER USING SEAFLOOR SYSTEM

## Slide 10: Advantages of seafloor direct push —Like pushing on land
Testing starts at the mudline
  measure the strength and deformation properties of very soft muds
Probes are pushed at a constant 2 cm/sec rate—meets ASTM D5778 for CPT and D6635 for DMT Specifications
  Waves do not alter this rate or cause pinching of cables
Rod pushing avoids zone between barge deck and mudline of parasitic rod buckling or lateral movement of casing
3-inch casing attached to the top of the seafloor system and extended to the barge deck serves as fixed reference to measure the tests depths
  does not move with either waves or the tide and provides accurate measurements
  attached hydraulic and air hoses to casing

## Slide 11: P-Y analyses from Dilatometer sounding

## Slide 12: vertical pile capacity from CPT sounding

## Slide 13: Pressuremeter tests
Used Texam Unit and performed strain controlled tests
  About 40 data measurements/test
Measured pressures with a digital gauge—accurate to 1 kPa
Used 74 mm tri-wing bit for cohesive soil and 76 mm tri-cone bit for cohesionless/cemented soil
  High quality borehole critical—experienced drillers important

## Slide 14
Chart: Corrected Pressuremeter Test Results
| 0 | 0.89947208862071193 | 1.8148372564761095 | 2.7123666184338147 | 3.5786912309591745 | 4.3834970347804925 | 5.090917609901946 | 5.7571161761696965 | 6.4166712789398117 | 6.4105125715461009 | 6.3576064286733569 | 6.255090532695351 | 6.3655752046421155 | 6.4676452151565478 | 6.577574540956066 | 7.1908981918616721 | 7.9349218943756794 | 8.6377892492690336 | 9.3853379064370301 | 10.14400824693773 | 10.161304387969739 | 10.129036156285732 | 10.092037469538084 | 10.115888563175846 | 10.144950244800599 | 10.22866625471519 | 10.927017154803732 | 11.714746487217486 | 12.494100776240892 | 13.29209956390962 | 14.071956390289397 | 14.092579200320987 | 14.083150411053214 | 14.041535670745686 | 14.047625653293338 | 14.069020730456128 | 14.161642166260545 | 14.876304096445004 | 15.647754010126636 | 16.431924821020893 | 17.209851516531536 | 17.981409759545986 | 18.750171194786059 | 19.524018932946706 | 20.286081906364693 | 21.03754908802642 | 21.795184002410473 | 22.550282564930193 | 23.300282642971439
Corrected PMT Results | 8.4345 | 8.6125 | 8.8305 | 9.3945 | 10.7945 | 14.1345 | 20.7705 | 28.7265 | 36.7685 | 27.6315 | 21.8645 | 17.9155 | 22.6445 | 26.9215 | 30.9085 | 40.4565 | 45.0545 | 50.9925 | 55.0905 | 58.5785 | 48.4115 | 41.9645 | 35.3975 | 43.6545 | 50.5515 | 55.3885 | 60.9465 | 62.9245 | 65.0165 | 66.1785 | 67.8305 | 57.4825 | 50.0645 | 43.9165 | 52.7945 | 59.9525 | 64.3305 | 68.3125 | 69.8745 | 70.7265 | 71.6185 | 72.5625 | 73.4185 | 73.8645 | 74.5865 | 75.5485 | 76.0645 | 76.4945 | 76.9445

## Slide 15: Vane shear tests
Used AP van den Berg I-VANE
Vane Motor at bottom of hole turned vane and measured torque
  No parasitic rod friction
Computer at surface read values from connecting cable and displayed results while performing test
Peak: turned vane 0.1o/sec for ¼ revolution
Rapid turning 6o/sec for 10 revolutions
Remolded: turned vane 0.1o/sec for ¼ revolution

## Slide 17: Standard penetration tests
Used 125 mm diameter steel casing telescoped inside 200 mm diameter steel casing
Added bentonite and polymers to the river water to make drilling mud—added soda ash to reduce the pH
Used NWJ drill rods (35 mm ID) for good mud circulation
Drill rods and Steel Casing were quite heavy for drill crew to maneuver
  Used crane on barge to either lower or remove them from hole
  Drilled lowered front jacks moving drill derrick out of way
  Crane could handle 110 feet (34 m) with each of its two hoists
Crane significantly improved efficiency of drilling/sampling operations

## Slide 18: True interval seismic test

## Slide 19: Example Seismic Waves
RECORDED WAVES
REPHASED WAVES

## Slide 20: True interval Seismic tests
Contract required both compression and shear seismic tests to 55 meters below mudline
  Compression waves measured the speed through incompressible water (1500 m/s—wasteful)
Cemented layers prevented penetration from top to bottom
Drilled 125 mm hole to 56 m
Lowered SDMT probe to 55 m carefully aligning sensors
Backfilled with washed fine gravel about 5 m above test
Performed seismic tests (multiple strikes) and then raised probe 1 m for next test
Used large hammer from seafloor to generate waves

## Slide 21
Dilatometer penetration causes has much smaller shear and volumetric strain to soil

## Slide 22: Standard Penetration Test
Predicting modulus from N-value has wide range of correlation factors
1) the energy not being measured
2) dynamically penetrating the soil
3) the soil being strained to failure
4) remolding of the soil
Best case for SPT:
Using N60 values in sand
Coeff. Of Var. =0.67 – quite high
For 95% certainty sett less than 25 mm,
then ave sett =7.5 mm

## Slide 23: Cone Penetration Test
Wide scatter of a factor to obtain deformation modulus from tip resistance
1) straining the soil to failure
2) remolding the soil
3) stress history unknown
Need site specific correlation values to get modulus

## Slide 24: Dilatometer Test
Advantages:
Economical to perform numerous tests at close intervals
Strains soil to intermediate levels similar to the structure
Measures the effect of soil stress history
Computation error when one uses an average M value for a layer—make layers same thickness as test interval

## Slide 25: PRESSUREMETER Chart for alpha
Baud and Gambin, 2013

## Slide 26
SOUTH END OF RIVER CHANNEL
Enlarged scale for upper 15 meters

## Slide 27
SOUTH END OF RIVER CHANNEL

## Slide 28
NORTH END OF RIVER CHANNEL
Enlarged scale for upper 15 meters

## Slide 30: conclusions
Seafloor direct push system efficiently pushed DMT and CPT—like performing them on land—the way to go!
Successfully measured seismic waves with true-interval seismic DMT probe and seafloor hammer to 55 meters below mudline
Undrained shear strength and deformation modulus values compared favorably with DMT, PMT, VST and CPT with properly chosen correlation factors
Adjust the investigation as data are collected
  1939 data—inadequate—show sandstone instead of cemented sand layers
  Upper clays much softer than thought
  Lower soil much stiffer and stronger than thought—needed more pressuremeter tests
Ideally, investigations could include direct push sounding and soil boring adjacent to each other and performed simultaneously
  If direct push sounding has penetration refusal before desired depth, perform pressuremeter tests in boring to get high quality data in that missing in-situ test zone
  Best use of costly barge time

## Slide 31: Thank You Questions?
GeoVirginia Conference April 9-11, 2018
in Williamsburg